Analysis appendix
# Data Tables
8cm CCW		8cm CW
volts (V)	current (A)	volts (V)	current (A)
148.5	1.355	148.3	1.248
168.6	1.446	168.4	1.325
187.9	1.520	188.1	1.400
207.7	1.604	208.0	1.474
227.9	1.674	228.2	1.546
247.5	1.752	247.8	1.613

10cm CCW		10cm CW
volts (V)	current (A)	volts (V)	current (A)
149.0	1.117	148.6	0.960
168.6	1.177	168.9	1.021
188.0	1.234	187.6	1.089
208.2	1.301	208.3	1.165
227.6	1.367	227.4	1.205
248.1	1.422	248.0	1.260

Table 1: Current through Helmholtz coils required to maintain 8 and 10cm beam diameter, respectively, for given anode-cathode voltages (resulting in different beam velocities), in clockwise (CW) and counter-clockwise (CCW) orientations.
# Variables and Equations
Variable	Name	Value and/or SI Unit
V	Voltage applied to anode	kg cdot m ^ 2 cdot s ^ -3
I	Current through Helmholtz coils	C cdot s ^ -1
K	Coefficient determining field strength at coil center	(7.73 +- 0.04) cdot 10 ^ -4 T cdot A ^ -1
R	Radius of Helmholtz coils	0.154 +- 0.005 m
K rsub R	Effective flux density for given distance from center of coils	%alpha T cdot A ^ -1, %alpha in [0, 1]
B rsub T	Total effective field in Helmholtz coils	T
B rsub E	Field contributed by Earth’s magnetic field	T
B rsub l	Field contributed by current in coil	T
I rsub l	Current in high-current orientation for measurement pair	C cdot s ^ -1
I rsub s	Current in low-current orientation for measurement pair	C cdot s ^ -1
r	Radius of electron beam	m

Table 2: Variables used in all equations and analysis
An electron traveling through a potential difference of V Volts gains kinetic energy
eV = 1 over 2 mv ^ 2
If the electron then travels through a uniform magnetic field vec B , a force e vec v times vec B acts on the electron. Assuming the direction of travel is exactly perpendicular to the field lines of vec B , we have
evB = mv^2 over r
 Rearranging and combining, we get
e over m = {2V} over {B ^ 2 r ^ 2} .
A series of anode voltage and Helmholtz current data pairs are taken by increasing V, and maintaining the radius r constant. B is calculated using K rsub r I . These measurements are repeated for the same voltages with the apparatus rotated 180^o , such that the effects of the Earth’s magnetic field are counteracted and can be measured.
# Sample calculation
For V = 250, I = 1.6825 (average of CCW and CW measurement pair):
e over m = {2 cdot 250} over {7.73 cdot 10 ^ -4 cdot 1.6825 cdot 0.08} = 1.847 cdot 10 ^ 11
The real value is 1.76 cdot 10 ^ 11 , so this measurement is within 5% of the real value.