Lab 2 – Abstract
David Laeer – 20341480
The aim of this laboratory was to experimentally determine the capacitance, inductance and resistance of a capacitor and inductor, and compare these with measured values from a DMM. Values were obtained by constructing RL and RC circuits, and varying the frequency of an applied AC voltage. The inductor’s resistance was measured as R sub L = 25.49%OMEGA , compared to an expected value of 24.5 %OMEGA . The inductor’s inductance was measured as L = 10.15mH , compared to an expected value of 10.00mH. The capacitor’s capacitance was measured to be C = 0.4639%mu F , compared to an expected value of 0.464%mu F . The experiment was a success since all data except R sub L agree with the expected values within error. The increased resistance that was measured in the circuit may be attributed to parasitic resistance in the breadboard/wires.